## Slide 1: Digital Innovation in evaluation Application of Geographic Information Systems in impact evaluation and geospatial portfolio analysis of transport projects
Toshiyuki Yokota, PhD
Principal Evaluation Specialist
Independent Evaluation Department
Asian Development Bank

## Slide 2: Geospatial data
Sensing
Data Mapping
Layers of GIS
Application

## Slide 3: #1 Geospatial Portfolio analysis

## Slide 4: Step 1: Digitize projects
Note: This presentation does not show any borderlines.
Figure 1: Locations of 163 Projects
Example: ADB financed 163 projects in 10 years

## Slide 5: Step 2: Overlap with other values
Note: This presentation does not show any borderlines.
Figure 2: Asian Highways and Project Locations
Example: 163 Projects and the Asian Highways

## Slide 6: Step 3: Set a Buffer zone
Figure 3: 10-kilometer Buffer Zone (Daytime and Nighttime)
Buffer zones can be set freely in size and shape.
Value in buffer zones can be measured if geospatial data are available.
Example: Road Project

## Slide 7: Measuring Population
Figure 4: Population in 2020 and Project Locations
Figure 5: Population in Buffer Zones by Country

## Slide 8: Co2
Figure 6: CO2 Emission from Transport and Project Locations
Figure 7: CO2 in Buffer Zones by Country
Figure 8: CO2 Density in Project Areas vs. Country Average
Project average
Country average

## Slide 9: #2 Impact analysis with Nighttime Light

## Slide 10: Difference In Differences = A–B
Pre-intervention
Post-intervention
A
B
With Project
Without Project
Figure 9: Difference of Difference
DID originated in the field of econometrics.
DID is typically used to estimate the effect of a specific intervention or treatment by comparing the changes in outcomes over time between the intervention group and a control group.

## Slide 11: project North–South Road Corridor in Armenia
Figure 10: Nighttime Light in 2015 and 2019

## Slide 12: Control Groups (Without project)
Figure 11: Two Control Groups
Control Road 1
Control Road 2

## Slide 13: Impact of Economic Development
Table 2: Growth Rate and DID
DID = difference-in-difference.
With Project | Without Project | DID
9.8% | 6.0% | 3.8%

## Slide 14: Impact assessment of 33 Completed Projects
Figure 12: Locations of 33 Projects

## Slide 15: Impact of Economic Development
Table 3: Average Annual Growth Rates of Nighttime Light of 33 Projects in Two Periods
With Project | Without Project | DID
11% | 6% | 5%
DID = difference-in-difference

## Slide 16: #3 Validation -triangulation-

## Slide 17: #1 With qualitative analysis
Document Review
  Manual
  AI
People’s Voice
  Beneficiary Survey
  e.g., North-South Road Corridor in Armenia
    Increased their access to markets and social service institutions
    Created employment opportunities
    Generated gender benefits (many women were engaged in agriculture activities or small or medium-sized agro-industries)

## Slide 18: #2 With quantitative analysis
EIRR measures benefits of travelers including time saving, vehicle cost saving, and reduction of accidents (Road users)
NTL measures socioeconomic activities in areas
(Local people)
Figure 13: Correlation between Growth Rate of NTL and EIRR
Positive correlation was observed, while it was not statistically significant yet.
e.g., economic analysis (EIRR)

## Slide 19: #3 with other GIS data
Figure 14: Increase in Nighttime Light and Population by Country
All Countries
Zoom in
e.g., Nighttime light VS. Population

## Slide 20: Conclusion
Performance
  Monitoring. Helping us monitor key socioeconomic indicators for SDGs such as economic growth, population, and CO2
  Impact evaluation. Help us measure attribution to local economic growth, and complementing the existing economic analysis
Advantage
  Evidence-base and Transparent
  Handy and real-time (Most data are free)
  Remotely and retrospectively accessible
  Comparable across countries as data quality and standards are same
Requirements
  Knowledge of GIS software like QGIS (Free app)
  GIS Data

## Slide 21: Thank you
https://journals.sagepub.com/doi/10.1177/03611981221092007

## Slide 22: Geospatial Datasets used
Table A: Geospatial Datasets Used

## Slide 23: case 1: DID = A-B Same time frame but different location
Pre-intervention
Post-intervention
A
B
Growth of the Project area
Growth of the Control group
4 years
Figure A: Difference of Difference (Case 1)
DID originated in the field of econometrics and uses a quasi-experimental design that makes use of data from treatment and control groups to obtain an appropriate counterfactual to estimate a causal effect.

## Slide 24: Case 2: DID = A-B Same location but different time frame
Pre-intervention
Post-intervention
A
B
Growth after the project completion
Growth before Project intervention
Figure B: Difference of Difference (Case 2)